## Slide 1: Applied Geographic Information Systems and GIS Programming
Yi Qiang （强毅）
Department of Geography
University of Hawaii - Manoa

## Slide 2
About Me
2017 – Now, Assistant Professor at University of Hawaii
2016 July – Dec, Research Associate at University of Colorado - Boulder
2013-2016, Postdoc at Louisiana State University
2012 Ph.D. in geography, Ghent University, Belgium
2007 M.Sc. in geographical information science, University of Edinburgh, UK
2006 B.Sc. in geographical information systems, Beijing Normal University, China

## Slide 3: My research interests
GIS
Geovisualization
Geocomputation
Spatio-temporal modeling
Resilience & Sustainability
Environment Modeling
Natural Hazard
Fundamental research
(GIScience)
Practical research
(GISystems)

## Slide 4: What is GIS
What is GIS?
Why you want to study GIS?
How do you use GIS in your study/research?

## Slide 5: What is GIS
GIS refers to GIScience or GISystem
The former focuses on methodology, and the latter focuses on the tools and systems that support the methodology
GISystem: A computer system that collect, manage, model, and analyze geospatial data to understand relationships, patterns, and trends in the data.
GIScience: the scientific discipline that studies geospatial data structures and computational techniques to capture, model, process, and analyze geographic information.

## Slide 6: Where GIS can be applied
Urban and regional planning
Natural resource management
Transportation and logistics analysis
Natural disaster mitigation and adaptation
Emergency management
Terrain analysis
Public health and epidemiology analysis
Millitary
and more…

## Slide 7: What GIS does? - A Day with GIS
7:00am, my alarm clock goes off… The energy to power the alarm comes from the local energy company, which uses a GIS to manage all its assets (e.g. electrical conductors, devices, and structures) so that it can deliver electricity continuously to customers.

## Slide 8: What GIS does? - A Day with GIS
7:15am, I jump in the shower… The water for the shower is provided by the local water company, which uses a hydraulic model linked to its GIS to predict water usage and ensure that water is always available to it customers.

## Slide 9: What GIS does? - A Day with GIS
8:00am, I plan my travel to my office… I turn on my smart phone to check the traffic condition on my way to office. It turns out there is a long pipe-up on the highway from my home to office. The GIS in the App suggests that taking a bus is faster than driving.
Real-time traffic in GIS

## Slide 10: What GIS does? - A Day with GIS
8:15am, I catch the bus… At the station, the waiting times for different buses are displayed in a LED board using the real-time locations from GPS installed in the buses. I can also check this information as well as current locations of buses from an App in my smart phone.
Bus waiting time at bus station
Tracking bus location in a mobile App

## Slide 11: What GIS does? - A Day with GIS
8:45am, I arrived at my office… I work at a grocery company (e.g. Walmart). The manager is call for a meeting to discuss the location of a new branch. We have invited a GIS consultant company to assess the best location of the new store, which will be close to our potential customers and have lowest land price and building cost.
Accessibility to grocery stores

## Slide 12: What GIS does? - A Day with GIS
11:45am, I feel hungry… I am ordering my lunch from Domino Pizza. The manager use a GIS to figure out which deliveries should go out together and plan the best delivery route for the delivery staff.
Use GIS to plan delivery route

## Slide 13: What GIS does? - A Day with GIS
5:00pm, I am off work. I plan to have dinner with some friends at a certain place. I use GIS to search for restaurant near that place and plan my route to the restaurant.
Query for restaurants near a location in GIS
Checking for restaurant reviews contributed by volunteer users

## Slide 14: GIS in Planning
Finding suitable locations for different types of development, for instance, solar farm

## Slide 15: GIS in Hazard Mitigation
Use GIS to assess risk, exposure, and vulnerability to flood, wildfire and sea level rise

## Slide 16: GIS in Hazard Mitigation
Use GIS to assess risk, exposure, and vulnerability to flood, wildfire and sea level rise
Precipitation
Slope
Land cover type
Land slide risk

## Slide 17: GIS in Environment Conservation
Use GIS to find suitable habitat of certain species – guide delineation of conservation area or wildlife refuges.
EA3692652

## Slide 18: GIS in Emergency Management
Manage and allocate assistance resources to reach the destination efficiently
Delineate functional zones to facilitate evacuation and recovery
The mapping center within the EOC was equipped with 20 GIS workstations and five plotters.
September 11, 2001
DEM post-911

## Slide 19: Public Participation GIS and Volunteer GIS
Creating a free editable map of the world by numerous volunteer users. (typical example: OpenStreetMap)
Map data is collected from scratch by volunteers performing systematic ground surveys using tools such as a handheld GPS unit, a notebook, digital camera, or a voice recorder.

## Slide 20: GIS and social media

## Slide 21: Typical scientific questions in GIS
Rational, effective, and efficient allocation of resources, in accordance with clearly stated criteria
Monitoring and understanding observed spatial distributions
Understanding the difference that place makes – identify which characteristics are inherently similar between places.
Understanding dynamic processes in the natural and human environments, such as processes of coastal erosion or urban growth
Support location-based decision-making – answering questions about where using data from multiple sources.

## Slide 22
GIS Programming
Part I: Python
Object-oriented programming
Syntax of Python
Python interface and modules in ArcGIS
Part II: GIS Data Access Using Python
Working with vector data
Working with raster data
Part III: Advanced GIS Modelling in Python
Automation of GIS processing tools
Dynamic modeling in GIS
Applied GIS
Part I: Principles
An Introduction to GIS
Representing the World in GIS
Part II: Techniques
GISystems
Geospatial Data
Geodatabase
Part III: Analysis
Cartography and Map Production
Geovisualization
Spatial Analysis
GIS Modeling

## Slide 23: Course Structure
No prerequisite knowledge in GIS or programming
Combination of theories, applications and case studies
Including both lectures and lab exercises
Develop hands-on skills in GIS analysis and modeling
Getting started with Python Programming in GIS

## Slide 24: Course Regulation
Do
Speak English in Class
Ask anytime when you have questions (raise your hands)
Open discussion is encouraged (raise your hands)
Contact me after class
Do not
Be late (>15min late deemed as absence)
Talking
Use cell phone in class (mute your cell phone)
Other disruptive behavior
Speak Chinese

## Slide 25: My contact information
Email: yiqiang@Hawaii.edu
Website: qiang-yi.github.io
Course materials (lectures and lab exercises): https://github.com/qiang-yi/NUAA

## Slide 26: Topic 2: Data Representation in GIS
We all live on the surface of the Earth, and spend most of our lives in a relatively small fraction of it.
Almost all human activities require knowledge about the Earth that are outside of our direct experience.
Traditionally, the knowledge about the Earth is documented in verbal description (book), visual description (maps), or in our brain (mental concept we began to develop as young children).
In digital representation (GIS), the knowledge of the Earth is formalized as data models – the structures and rules that accommodate data.

## Slide 27: Data representation in GIS
An atom of geographic data (i.e. a datum) consists of a space, a time and some descriptive properties (attributes), for instance,
  “The average income at Boulder, CO in 2014 is $69,407”
  “The elevation (m above sea) at latitude 27.986065, longitude 86.922623 is 29,029m, which was measured in 1955.”
  “State of Hawaii vote for Democratic Party in 2016 US presidential election”
Where
When
What
Three Ws in geographic data

## Slide 28: Types of Attributes
Nominal: the simplest type of attribute, serves only to identify or distinguish one entity from another. For example, place names or house number.
Ordinal: values that have a natural order. For instance, Canada rates its agricultural land by classes of soil quality, with Class 1 being the best, Class 2 not so good, etc…
Interval: if the difference between values make sense. For instance, Celsius temperature is interval attribute, because 30°C and 20°C is as different as 20°C and 10°C
Ratio: if the ratio between values make sense. For instance, weight is ratio, because 100kg is twice as 50kg.

## Slide 29: Representation of Time
Time point: a point on the time line, e.g. Sept. 11, 2001 or 19:51:32
Time interval: an extent on the time line, e.g. from 1949 to 2017, from 9:00am to 17:00pm.
Time cycles: a repeating point or interval along the time line, e.g. every Monday afternoon.

## Slide 30: Representation of Space
The two fundamental ways of representing space are discrete objects and continuous fields.
The discrete view: the world is empty, except where it is occupied by objects with well-defined boundaries that are instances of generally recognized categories, for instance, a house, a lake, a car or a people on the Earth surface.
An discrete object can be represented as a point, lines, or polygon, or polyhedrons (3D)

## Slide 31: A discrete world
Points
Lines
Polygon
3D polygons

## Slide 32: The continuous view
Some geographic processes do not have discrete boundaries, e.g., urban area, freshwater wetland, Chinatown.
The continuous field view represents the real world as a finite number of variables, each one defined at every possible position.
Digital elevation data

## Slide 33: Rasters and Vectors
Continuous and discrete are two conceptual views of the world.
Raster and vector are two digital representations of the world in GIS.
Strictly speaking, both raster and vector can model continuous and discrete world. However, raster is more associated with the continuous view, while vector is more used for the discrete view.

## Slide 34: Vector model
Vertices
Polygon
Points
Nodes
Line
X
Y
Features are stored as a series of x-y coordinates in a rectangular coordinate system.
Many different coordinate systems may be used.

## Slide 35: Features linked to data
Each feature is linked to an entry in a data table containing information about the feature.

## Slide 36: Advantages of vectors
Precise location of features
Storing many attributes
Flexible for cartography
Compact storage of information
Ideally suited for certain types of analysis, especially areas, lengths, connections

## Slide 37: The raster data model
Rows
Columns
X, Y location
Raster data file
N rows by M columns
X, Y location
Georeferenced to earth’s surface

## Slide 38: Raster and Vector Data
Point
Line
Polygon
Vector
Raster
Raster data are described by a cell grid, one value per cell
Zone of cells
Notes: DRM

## Slide 39: GIS data models
Vector model
Raster model

## Slide 40: Types of raster data
Discrete raster: land use
Continuous raster: DEM
Continuous raster: image
Discrete raster: roads

## Slide 41: Continuous data
Raster is the best way to store continuously changing values such as elevation
Analysis faster and more flexible than vectors for many applications
Some analysis only possible using rasters

## Slide 42: Raster analysis functions
Density
Least cost path
Distance
Interpolation
Viewshed
Buffers

## Slide 43: Impact of resolution
Storage space increases by the square of the resolution
Portraying large areas at high precision is problematic
90m resolution
10m resolution

## Slide 44: Storage of attributes
Roads may have other attributes: ownership, speed limit, number of lanes, etc.
Would need a new raster for each attribute
Only numeric attributes may be stored
Raster contains 1 value indicating a single attribute—road type for example

## Slide 45: The raster data model
Rows
Columns
X, Y location
Raster data file
N rows by M columns
X, Y location
Georeferenced to earth’s surface

## Slide 47: Digital Raster Graphic

## Slide 48: Converting Vector to Raster Data is Easy

## Slide 49: Converting Raster Data to Vector is Hard Nearly Impossible

## Slide 50: Issues w/ Raster & Vector