## Slide 1: Applied Geographic Information Systems and GIS Programming Day 2: Spatial Analysis using Vector Data
Yi Qiang
Department of Geography
University of Hawaii - Manoa

## Slide 2: Course evaluation
4 lab exercise (15% * 4)
  Finish the exercises in the computer lab
  Finish by yourselves and don’t copy others
  Submit answers no later than 11:59pm the next day
  Submit in Microsoft Word file format
1 project (30%)
Attendance (10%)

## Slide 3: Recall of the previous class
Three components of GIS data: space (where), time (when), and attributes (what)
Vector data and attribute table
Where
When
What
Three Ws in GIS data

## Slide 4: Recall of the previous class
Two representation of the world
  The discrete world: discrete objects with clear boundary in an empty space
  Continuous world: a continuous field where every location has a value
Two GIS data types
  Vector: point, lines, and polygons, mostly used to model discrete objects
  Raster: grid of cells (pixels) with equal size and shape, mostly used to model continuous field

## Slide 5: Discrete objects in vector data
Vertices
Polygon
Points
Nodes
Line
X
Y
Vector object is formed by points or series of points

## Slide 6: Only keeping the location of nodes is not enough
1 polygon or 2 polygons?

## Slide 7: Spatial topology
Topology is concerned with the properties of space that are preserved under continuous deformations, such as stretching, crumpling and bending.

## Slide 8: Königsberg’s Seven Bridge Problem
Find a walk through the city that would cross each of those bridges once and only once.

## Slide 9: Simplify the problem
Solved by Leonhard Euler

## Slide 10: Topology
In GIS, topology refers to the relative spatial relations between features.
Topology is about how features are connected and which features are adjacent to each other.
Topology distinguishes GIS data models from non-topological data models supported by many CAD, Photoshop and other graphics systems

## Slide 11: Topology
Can be viewed as a mathematical procedure that determines spatial relationships and properties, including:
  The three Cs
    Connectivity (Highway US 75 connects to IH 45)
    Coincidence--same location (Red River & TX/OK border)
    Contiguity--adjacency or “next door” (TX & OK)

## Slide 12: Topology Type I: Arc-node topology
  Nodes are the end-points of arcs. Arc-node topology keeps track of which arcs are connected to other arcs through shared nodes X It defines length, direction, and connectivity for arcs.
  The from-node is an arc’s starting point; the to-node is its ending point.
    They are determined as you digitize your data.
    You can tell the from-node and to-node by its order.
    Arcs connect if they share a node.

## Slide 13: Topology Type II: Polygon-arc topology
  Polygon-arc topology expresses the relationship between the arc features and the polygon features for which the arcs create boundaries. It defines area and adjacency. A set of arcs that form a closed figure define the area of a polygon. Polygons are stored as a list of arcs to avoid redundancy. Two polygons are adjacent if they share an arc.

## Slide 14: Topology Concept III Left-right topology
  Left-right topology refers to contiguity -- how polygons are associated with their neighboring polygons. Each arc has a list of which polygons are on the right side and which are on the left side. GIS uses this information to determine from one polygon what the adjacent polygons are:
1
2
3
4
5
6
7

## Slide 15: Auto-complete Polygons
Why we need topology in GIS

## Slide 16: Why we need topology in GIS
Using topology to prevent editing errors

## Slide 17: Represent adjacency (Common Border)
The primary purpose of a topology is to define spatial relationships between features
Why we need topology in GIS

## Slide 18: Preserving Coincidence
Why we need topology in GIS

## Slide 19: Preserving Connectivity
Why we need topology in GIS

## Slide 20: Common Topology Elements
Both edge and node are treated as single elements
  Multiple copies of them stored in the GIS data are deleted as if they were one

## Slide 21: Topological relations

## Slide 22: Query in GIS
The process of selecting information from a GIS by asking spatial or logical questions of the geographic locations OR attributes.
Basic query operations may be combined to select complex sets of information - similar syntax as SQL language
  Query by attributes (attribute query)
    What is found at a location (what is where)
Query by location (spatial query)
  Where can you find a feature (Where is what)

## Slide 23: Examples of Queries
Find me all the land parcels that
  Are in Syracuse, NY
  That are at least 2 Acres in size
  That changed hands in the last 2 years
  That have a assessed value of at least 1 million
  That are classed residential

## Slide 24: Query by attribute
Make selections according to the values in attributes.
For example, select all states that have population larger than 10 million, POPULATION >= 10,000,000

## Slide 25: Query by attribute
Multiple queries can combined using logical operator, such as AND, OR, NOT
For example, select all states where male is more than female and population is larger than 5 million, "POP2010" > 5000000 AND "MALES" > "FEMALES"

## Slide 26
Query by location (Spatial query)
Also called spatial selection, a special type of database query supported by geodatabases and spatial data types.
Identifying features based on spatial criteria, for example, adjacency, connectivity, containment, arrangement
Select states that are adjacent to Missouri

## Slide 27
Adjacency depends on the algorithm used
(the same is true for all spatial operations)

## Slide 28
Touch the boundary of
Share a line segment with
Different Adjacency in ArcGIS

## Slide 29
Spatial Selection
Identifying features based on spatial criteria
Adjacency, connectivity, containment, arrangement

## Slide 30
Selection based on spatial and non-spatial attributes

## Slide 31: Creating and Editing Vector data
Creating vector features
  Creating vector geometries
Splitting vector features
  Splitting lines
  Splitting polygons
Combining features
  Merge
  Union
  Intersect
Auto-complete polygons

## Slide 32: Create Vector Geometries

## Slide 33: Multi-part Features

## Slide 34: Splitting Lines

## Slide 35: Splitting Polygons

## Slide 36: Union

## Slide 37: Edit the attribute table
Edit the attributes associated with the vector geometries

## Slide 38: Spatial Analysis in GIS
Identify relationships between or among features and/or layers
Spatial analysis is useful for evaluating suitability and capability, for estimating and predicting, and for interpreting and understanding.
Spatial Overlay is the key method of spatial analysis, which combines information of multiple layers into a new layer.

## Slide 39: Spatial Overlay
For vector data, the most common overlay methods are
  Clip- the cookie cutter
  Erase-the eraser shield
  Intersect-keeps data from both data sets
  Union- keeps everything from every data set

## Slide 41: Buffer Analysis
Also known as proximity analysis, creating a zone of interest around an vector feature, or set of vector features.

## Slide 42
Creating buffer zone
Point
Line
Area

## Slide 43
3 km Buffer Zones Around Railway System

## Slide 44
Distance Surface
125 m Buffer Zones
Proximity maps for points of interests

## Slide 45: Summary
Topology
  Spatial relations that preserves under continuous deformations
  The foundation of spatial query and analysis
Queries in GIS
  Query by attribute
  Query by location (spatial query)
Creating and Editing Vector data
Spatial Analysis
  Spatial Overlays – Union, Intersect, Clip, Erase
  Buffer – proximity analysis